## Slide 1
DA 1 · PROJECT OVERVIEW
Intelligent Router Path Selection using Machine Learning
Routing on predicted path quality instead of static metrics
github.com/K-RANGARAJAN/smart-path-selector
Notes: Introduce the project: traditional routing protocols pick paths from fixed numbers. This project predicts how good each path will actually be, and routes on that.

## Slide 2
THE PROBLEM
Routing protocols decide on static numbers
R
RIP
DECIDES ON
Hop count
Fewest routers wins
BLIND TO
Link speed, load, delay, loss
O
OSPF
DECIDES ON
Configured cost
Reference bandwidth ÷ link bandwidth, Dijkstra
BLIND TO
Congestion — the cost never changes at runtime
B
BGP
DECIDES ON
Policy & AS-path
Local preference, shortest AS path
BLIND TO
Performance of the path altogether
DA 1 · Project overview
2
Notes: RIP counts hops. OSPF uses a configured cost tied to bandwidth. BGP follows business policy. None of them measure what the path is doing right now.

## Slide 3
WHY IT MATTERS
“Best” on paper, worst in practice
A
B
4 hops · 10 Gbps · congested
5 hops · 1 Gbps · idle
Static protocols pick
The amber path
Fewer hops (RIP) and lower cost (OSPF), even while it drops packets.
Measurements say
The teal path
Longer on paper, but lower delay and no loss right now.
Illustrative scenario
DA 1 · Project overview
3
Notes: A concrete case: the 10 Gbps backbone is shorter and cheaper by OSPF cost, but it is carrying a traffic spike. Traditional routing keeps sending traffic into it.

## Slide 4
PROPOSED SOLUTION
Predict each path’s real quality, then route on it
Latency
Available bandwidth
Packet loss
Jitter
Hop count
Live metrics per candidate path
Random Forest regression
learns how metrics translate into next-interval quality
Quality score per path
Path 1
91
Path 2
74
Path 3
38
Highest score is recommended
DA 1 · Project overview
4
Notes: Instead of a fixed metric, a model trained on measured metrics outputs a 0–100 quality score per candidate path. The recommendation engine picks the best one. Scores shown are an example.

## Slide 5
DESIGN
System architecture
1
Network simulator
Multi-AS topology, time-varying traffic, congestion events
2
Dataset
Measured metrics now → realised quality next interval
3
ML model
Random Forest regressor, quality score 0–100
4
Path recommender
Scores candidates, picks best, avoids flapping
5
Dashboard
Live metrics, scores and decisions
Baselines on the same topology
RIP
OSPF
BGP
compared on identical traffic
Validation (optional)
Cisco Packet Tracer ping / tracert outputs scored by the trained model
DA 1 · Project overview
5
Notes: Five stages from simulation to dashboard. RIP, OSPF and BGP decision logic run on the same topology and traffic so the comparison is fair. Packet Tracer is used to sanity-check on a real configuration.

## Slide 6
DATA
What the model sees, and what it predicts
Feature | Meaning
Latency (ms) | End-to-end delay: propagation + queueing
Available bandwidth (Mbps) | Spare capacity at the path’s bottleneck
Packet loss (%) | Probes lost along the path
Jitter (ms) | Variation in delay
Hop count | Number of links — what RIP uses
Trends | Change since the last measurement
TARGET
0–100
Path quality score in the next interval
Combines delay, jitter and loss (ITU-T G.107 E-model) with whether the path has enough bandwidth for the flow.
DA 1 · Project overview
6
Notes: Inputs are the metrics a router can measure with probes. The target is the quality the path actually delivers in the next interval, so the model is predicting, not just re-computing.

## Slide 7
MODEL CHOICE
Why a Random Forest
1
Non-linear
Loss and delay explode as a link nears saturation; trees capture thresholds without hand-tuning.
2
Robust to noise
Averaging many trees smooths noisy probe measurements.
3
Fast
Scoring a handful of paths takes well under a millisecond.
4
Explainable
Feature importance shows which metrics drive decisions.
DA 1 · Project overview
7
Notes: Linear regression will be used as a comparison point; it cannot represent the sharp degradation near saturation.

## Slide 8
EVALUATION PLAN
How success will be measured
Prediction accuracy
R² on unseen traffic
Mean absolute error
Root mean squared error
vs linear regression and a no-ML formula
Routing quality
Mean realised path quality
Latency and packet loss
% of time with poor quality
Route changes (stability)
Every strategy — ML, RIP, OSPF, BGP — routes the same flows through the same simulated traffic.
DA 1 · Project overview
8

## Slide 9
EXECUTION
Tools and plan
Stack
Python
simulator & pipeline
NetworkX
topology, paths
scikit-learn
Random Forest
pandas / NumPy
data
Flask
dashboard
Packet Tracer
validation
Milestones
1
DA 1 · Now
Problem, design, plan
2
DA 2 · 50%
Simulator, dataset, protocol baselines, trained model & metrics
3
Final · 100%
Recommendation engine, full evaluation, live dashboard demo
DA 1 · Project overview
9

## Slide 10
EXPECTED OUTCOME
Routes that follow real network conditions, with measurable gains over RIP, OSPF and BGP
Higher average path quality
Less time on congested paths
Stable routing without flapping
Thank you